## Slide 1
RAGHU ENGINEERING COLLEGE
(AUTONOMOUS)
DEPARTMENT OF EEE
Academic year: 2018-2019
II year 2-semister
Digital Electronics
CASE STUDY
ON
TO DESIGN THE CIRCUIT FOR THE EXPRESSION Y=A’B+C’D AND DO THE DELAY ANALYSIS IN ALL POSSIBLE REALISATIONS.
BATCH-10
18985A0246 – K.Karthik
18985A0247 – L.Ratnakara Rao
18985A0248 – M.Gaddim Naidu
18985A0249 – M.Jagapathi varma
18985A0250 – M.Sai
FACULTY:
Mr.D.Bhaskar Rao
Associate professor

## Slide 2: Design Task
Case study on design the circuit for expression Y =A’B + C’D and do the delay analysis in all possible realisation

## Slide 3
Design Restriction
4 bits are majority
Design Goal
To design a circuit which as delay time by examining possible realizations.

## Slide 4
Design options:
We can do this by 4 realizations namely:
SOP Realization.
POS Realization.
NAND Realization.
NOR Realization.

## Slide 5: Circuit Diagram
The circuit diagram of given expression :
Expression : A’B +C’D

## Slide 6
OR Gate- 74ls32
NOT Gate- 74ls04
AND Gate- 74ls08

## Slide 7
S.NO | PATH | TWO INPUT NOT | TWO INPUT AND | TWO INPUT OR | DELAY TIME In (nanosec) | TOTAL DELAY In (nanosec) | MAXIMUM DELAY In (nanosec)
1 | A-Y | 1 | 1 | 1 | 15+18+15 | 48 | 48
2 | B-Y | - |  |  | 18+15 | 33 | 
3 | C-Y | 1 | 1 |  | 15+18+15 | 48 | 
4 | D-Y | - |  |  | 18+15 | 33 | 
DELAY ANALYSIS FOR SOP REALISATION

## Slide 8: Nand Realisation

## Slide 9
2 input NAND Gate-74ls00

## Slide 10
S.NO | PATH | TWO INPUT NAND | DELAY TIME | TOTAL DELAY | MAXIMUM DELAY
1 | A-Y | 3 | 3*15 | 45 | 45
2 | B-Y | 2 | 2*15 | 30 | 
3 | C-Y | 3 | 3*15 | 45 | 
4 | D-Y | 2 | 2*15 | 30 | 
DELAY ANALYSIS FOR NAND REALISATION

## Slide 11
POS Realisation
Expression : (A+B’).(C+D’)

## Slide 12
OR Gate- 74ls32
NOT Gate- 74ls04
AND Gate- 74ls08

## Slide 13: DELAY ANALYSIS FOR POS REALISATION
S.NO | PATH | TWO INPUT NOT | TWO INPUT AND | TWO INPUTOR | TIME DELAY | TOTAL DELAY | MAXIMUM DELAY
1 | A-Y | 1 | 1 | 1 | 18+15+15 | 48 | 63
2 | B-Y | 2 | 1 | 1 | 15*2+18+15 | 63 | 
3 | C-Y | 1 | 1 | 1 | 18+15+15 | 48 | 
4 | D-Y | 2 | 1 | 1 | 15*2+18+15 | 63 | 

## Slide 14: NOR Realisation

## Slide 15
2 input NOR Gate- 74ls02

## Slide 16: DELAY ANALYSIS NOR REALISATION
S.NO | PATH | TWO INPUTOR | TIME DELAY | TOTAL DELAY | MAXIMUM DELAY
1 | A-Y | 3 | 3*15 | 45 | 60
2 | B-Y | 4 | 4*15 | 60 | 
3 | C-Y | 3 | 3*15 | 45 | 
4 | D-Y | 4 | 4*15 | 60 | 

## Slide 17: DELAY TIME EFFECTIVE REALISATION
S.NO | TYPE OF REALISATION | MAXIMUM DELAY IN NANO SEC
1 | SOP | 48
2 | NAND | 45
3 | POS | 63
4 | NOR | 60
We hereby conclude that NAND circuit is delay effective, whereas POS comes under the worst case i.e., with more delay.

## Slide 18: DESIGN FAILURE ANALYSIS
TYPE OF REALIZATION | NO. OF IC’s USED | HIGHEST PROBABILITY OF FAILURE
SOP | 3 | 2
POS | 3 | 
NAND | 2 | 
NOR | 2 | 
As the no. of IC’s used in NOR realization are 2, there is a less probability of occurrence of failure.

## Slide 19: CONCLUSION
All the realizations have been designed and verified using circuit lab software, and we conclude that NAND realization provides less delay when compared to all other realizations.

## Slide 20
REFERECE FOR DELAY TIME IS TAKEN FROM:
FAIR CHILD SEMICONDUCTOR
MOTOROLA .
GLOBAL ELECTRONICS.
ON SEMICONDUCTOR.
TOSHIBA.
PHILIPS